## Slide 1
Presentation to the C2SIM AXS Group
Elizabeth Hosang, July 2024
Overview of IEEE Robotics Standards
Notes: Welcome to CAE!

## Slide 2: Acronyms
AuR – Autonomous Robots
ALFUS – Autonomy Levels for Unmanned Systems
CORA – Core Ontology for Robotics and Automation
CORAX – CORA Extension. Aspects of reality necessary for modelling, but not explicitly covered by SUMO.
DOLCE – Descriptive Ontology for Linguistic and Cognitive Engineering
DUL – DOLCE ultra-light.
ORA – Ontology for Robotics and Automation
POS – Position and Orientation ontology
R&A – Robotics and Automation
SUMO – Suggested Upper Merged Ontology

## Slide 3: Presentation Overview
The purpose of this presentation is to evaluate 1872.2-2021 IEEE Autonomous Robotics (AuR) Ontology to see if it defines concepts that could be used in defining the C2SIM extension for Autonomous Vehicles.
AuR is an extension to 1872-15 IEEE Standard for Ontologies for Robotics and Automation, which defines the Core Ontology for Robotics and Automation (CORA).
CORA uses concepts defined in the Suggested Upper Merged Ontology (SUMO) (The Suggested Upper Merged Ontology (SUMO) - Ontology Portal).
AuR also uses SUMO, but it is not tied to an upper-level ontology. It also uses the Descriptive Ontology for Linguistic and Cognitive Engineering (DOLCE) ultra-lite (DUL). [2308.01597] DOLCE: A Descriptive Ontology for Linguistic and Cognitive Engineering (arxiv.org)
Therefore, to understand the concepts in AuR, we need to touch on the other standards.

## Slide 4: Standard Overview: Suggested Upper Merged Ontology (SUMO)
“Largest formal public ontology in existence today” (according to the website)
Contains concepts across multiple domains: Communications, Countries and regions, Distributed computing, User Interfaces, etc.
Useful concepts from SUMO, as identified in AuR:
  Attribute – Qualities that cannot be or are chosen not to define as subclasses.
  Case Role – Class of predicates relating the spatially distinguished parts of a process.
  Corpuscular Object – A self-connected object whose parts have properties that are not shared by the whole.
  Process – The class of things that happen and have temporal parts or stages.
  Proposition – Abstract entity that expresses a complete thought or set of thoughts.

## Slide 5: SUMO Key Concepts for CORA
Agent -> ActorEntity
  Passt auch bzgl. der Unterklassen, bei Agent gibt es Group, bei ActorEntity gibt es CollectiveEntity also fits regarding the subclasses, Agent has subclass Group and ActorEntity has subclass CollectiveEntity
Artifact -> SubClassOf PhysicalEntity (it strange though, that the LOX puts vehicles under platform)
  No direct mapping seems to fit, I would just make it a subclass of Physical Entity
Measure (the Object Property?) -> hasEntityState
Object -> Entity
Electric Device -> (we could just follow the path from Artifact)
Computer Process -> (what do we do with Process in general?)
Device -> see Electric Device
Group -> CollectiveEntity (although group has also superclass collection, so weaker relation for mapping?)
Measuring Device -> see Device, Electric Device

## Slide 6: Standard Overview: Descriptive Ontology for Linguistic and Cognitive Engineering (DOLCE)
“First top-level (foundational) ontology to be axiomatized”
Provides general categories and relations.
  Event – any physical, social, or mental process, event or state. -> C2SIM provides action and event, both are not defined though. I would suggest to map DOLCE:Event on C2SIM:Action, because this matches the subclasse of both ontologies a bit better
  Goal – Description of situation desired by an agent, usually associated to a plan that describes how to achieve it. -> Couldn’t find it in DOLCE
  Information Object – Any piece of information: musical composition, text, word, etc. independent from how it is concretely realized. -> Couldn’t find it in DOLCE
  Physical Object – Any object that has a proper space region. -> difficult, because Location and PhysicalEntity (best candidate though) are quite separated in C2SIM
  Quality – Any aspect of an entity that cannot exist without the entity, e.g. specific light of a place at a certain time. -> Seems to be missing in C2SIM
  Role – Concept that classifies an object. -> Couldn’t find it in DOLCE

## Slide 7: Standard Overview: IEEE 1872-2015 CORA
IEEE 1872-2015 Standard Ontologies for Robotics and Automation (CORA)
Covers basic concepts to describe robotics: parts, processing, environment, behavior, etc.
Uses concepts from SUMO: Object, Artifact, Agent, Group, Process, etc.
Defines CORAX: ontology defining aspects of reality that are necessary for modelling, but too general for SUMO or CORA.
  Examples: PhysicalEnvironment, Interaction (type of Process (SUMO), ProcessingDevice, etc.
Defines POS: Position and Orientation.

## Slide 8: Key Concepts from CORA (1/2)
Robot – Agent Device purposed to act in the physical world in order to accomplish one or more tasks. -> SubclassOf ElectricDevice (see Artifact)
Robot Part – Any device attached to a robot that serves in its functioning, e.g. Sensing, Communicating, Actuating, Processing -> Something like hasPart seems to be missing in general
CollectiveRoboticSystem – Two or more robots that are assumed to collaborate in some way to achieve a common goal. -> I know from the “swam discussion”, that it is not clear, how to define groups in C2SIM, so this is also very general
  Each may have its own goal that is a subgoal of the larger one.
  The robots may not communicate with each other directly, e.g. assembly line.
RobotGroup –> (see CollectiveRoboticSystem)
RoboticSystem –> (see CollectiveRoboticSystem)
RoboticEnvironment -> not sure about the exact meaning

## Slide 9: Key Concepts from CORA (2/2)
Roles: -> Not sure what those are in CORA
  Fully Autonomous
  Remote Controlled
  Automated – not adaptive,
  Teleoperated – human operator either directly controls or assigns incremental goals based on a continuous basis.

## Slide 10: Key Concepts from CORAX
Physical Environment -> Subclass of EnvironmentalObject
Interaction – not defined in SUMO -> Subclass of Event?
Artificial System -> again, there is no real concept for groups and partOf in C2SIM
Robot Motion – any process where a robot moves one of its parts -> Subclass of Event?
HumanRobotCommunication -> C2SIM offers CommunicationNetwork, maybe this is a connenction point
RobotRobotCommunication -> C2SIM offers CommunicationNetwork, maybe this is a connenction point

## Slide 11: Key Concepts in POS
PositionCoordinateSystem
PositionMeasure
PositionPoint
PositionTransformation – between two coordinate systems.
PositionRegion
-> C2SIM works with own concepts of Location, if those worked so far, they should be work for robotic systems, including some minor changes perhaps

## Slide 12: Key Concepts in AuR – Behavior Subtypes
Architectural behavior – Internal organization of the flow of information that determines the object’s behavior. Subtypes:
  Reactive
  Deliberative
  Cognitive
Emergent behavior – Set of relationships chosen to describe the object relevant interactions. Is an Information Object (DUL) / Proposition (SUMO)
Engineering behavior – Manifested behavior given by a set of state variables.
Manifested behavior – Evolution of the object’s qualities and the relationships holding among that object and any other objects participating in the event.
Rule behavior – Set of rules and decision methods that an agent has and can use to decide its actions.

## Slide 13: Key Concepts in AuR - Other
Function – Role that the manifested behavior of the object plays in an event.
Interaction
  Information Interaction
  Physical Interaction
  Manifested behavior
Object-centered environment
  Examples: environment of an industrial robotic arm is the location / spatial area that the robot can potentially reach during the time of an event.
Object-centered environment description
Physical Interaction

## Slide 14: Summary and Next Steps
Some of the concepts in the three referenced standards (SUMO, DUL and CORA) can be mapped to concepts in the C2SIM core models, e.g. Agent, Event, Physical Environment.
Concepts from AuR such as Behavior and Interactions also overlap with key C2SIM concepts.
Possible next steps:
  Identify concepts from these standards that may be relevant to Autonomous system use cases, e.g. communication between entities.
  Map these concepts against the C2SIM core model to identify concepts that lack corresponding entities in C2SIM.

## Slide 15
Thank you!